## Slide 1: TEAM NASHVILLE
Richard Desatnik, Katherene Qi, Divyangum Dutta, Boda Huo

## Slide 2: Intro
Research goal
Hardware Setup
Restoring the fisheye images
Image Stitching with SIFT
Learning and Recognition with YOLO
Path Planning
Summary and Conclusion

## Slide 3: Hardware
3 Robots
6 People
4 Shelves
1 Additional Obstacle
Warehouse size
  Height: 10.5m
  Width: 16m
  Length: 24.7m

## Slide 4: Fisheye Photos
Original image misses critical information
Fisheye covers area but is distorted
Image restoration with OpenCV
  cv2.fisheye.estimateNewCameraMatrixForUndistortRectify
  cv2.fisheye.undistortImage

## Slide 5
Matching Results
FlannBasedMatcher
Heuristic for good matches
  Lowe’s ratio test
cv2.findHomography()
cv2.warpPerspective()

## Slide 6
Notes: I think I’ll rerun the code for this to remove the white lines going across the image.

## Slide 7: Using YOLO
Annotated images using labeling in YOLO format.
Classify objects into Shelf, Person, Robot etc.
50 epochs with a batch size of 16.
Can save past training data + add more data / learning.
Class labels and Bounding boxes with coordinates

## Slide 8
Results and Confidence Scores

## Slide 9: Path Planning
Objective
  Enable robots to navigate around obstacles using path planning.
  Visualize the path overlay on the environment for verification.
Path Planning Technique
  Uses a shortest-path search algorithm on a binary cost-map.
  Avoids obstacles (high-cost areas) and finds the most efficient collision-free route.
  Optimized for real-time performance.

## Slide 10: Path Results

## Slide 11: Next steps (future work)
  Connect Robots + control them to move according to the path
  Live stitching → using video feeds
  Scaling to a bigger warehouse
  Integrating more cameras and mirrors

## Slide 12: Q & A